## Slide 1: I GeMA Workshop
13/07/2017

## Slide 2: Schedule
10:00 – Introduction to the GeMA framework (Carlos Augusto)
11:00 – Building simulation models (Carlos Augusto, Nilthson, Cristian)
12:00 – Lunch break
13:00 – Orchestration (Erwan)
14:00 – The ERAS portal (Maria Julia)
15:00 – Sabiah: Workflow for reservoir Geomechanics

## Slide 3: Introduction to GeMA
Carlos Augusto Teixeira Mendes
13/07/2017

## Slide 4: GeMA
Geo Modelling Analysis Framework
Framework x Application

## Slide 5: GeMA
Much has been done,
even more needs to be done,
but we already have several nice capabilities.
( at least we hope so! )

## Slide 6: Simulation Components
Model Data
Solution Method
Results Monitor
Simulation
Notes: Dados do Modelo = O que?
Método de Solução = Como?

## Slide 7: Simulation Components
Model Data
Solution Method
Results Monitor
Simulation
Lua Files
C++ Object
Interpretation
Notes: Vantagens uso arquivos Lua
Possibilidade de construção direto via API

## Slide 8: Executing a Simulation
Orchestration script execution
Physics
function script()
end
Orchestration Script
Model Data
Mesh
Boundary cond.
Properties
. . .
Solution Method
Orchestration script
. . .
GeMA
Results
Processes

## Slide 9: User Types
Modelo
Físico
Solution Method
Model Data
1
Orchestration script
Processes and Physics
External Simulators
Creates
2
3
User with knowledge of:
Mathematical model
Application domain
Numerical development
1
2
3
Creates
Creates

## Slide 10: User Types
Modelo
Físico
Solution Method
Model Data
1
Orchestration script
Processes and Physics
External Simulators
Creates
2
3
User with knowledge of:
Mathematical model
Application domain
Numerical development
1
2
3
Creates
Creates
4
GeMA

## Slide 11: Architecture
Based on two central concepts:
Plugins and Abstract interfaces
  Extensibility
  Modularity
Use of an extension language embedded in the framework core
  Flexibility

## Slide 12: Architecture – Plugins
GeMA Library
GeMA Application
Mesh
Plugins
Plugin Interface
Mesh Interfaces
Processes
Plugins
Plugin Interface
Process Interfaces
Physics
Plugins
Plugin Interface
Physics Interfaces
Numeric Solvers
Plugins
Plugin Interface
Num. Solver Interfaces
Properties
Plugins
Plugin Interface
Properties Interfaces
I/O
Plugins
Plugin Interface
I/O Interfaces
Uses
Extends

## Slide 13: Architecture – Extension Language
Lua
Model extension
  User functions
  Processes and physics can be implemented in Lua
Orchestration
Flexible model description
Ease integration with existing simulators

## Slide 14: Simulation Components
Model Data
Solution Method
Results Monitor
Simulation
Notes: Dados do Modelo = O que?
Método de Solução = Como?

## Slide 15: Model Data – What will be simulated ?
Model Data
User Functions
Boundary Conditions
Property Sets
State Variables
Meshes
Initial Conditions

## Slide 16: Meshes
Spatial model discretization
  A general term that includes several types of discretization
One model can have multiple meshes
Data associated to nodes and cells
Model Data
User Functions
Boundary Conditions
Property Sets
State Variable
Meshes
Initial Conditions

## Slide 17: Mesh Types
η
ξ
Mesh
Element Mesh
Topo Cell Mesh
Topo Element Mesh
Cell Mesh
Node Mesh
Cell Mesh with topology
Cell Mesh
Element Mesh

## Slide 18: Entities associated to a Mesh
Cell / Element
Border
Integration Points
Nodes
Group of cells (heterogeneous)
Ghost Nodes

## Slide 19: Data associated to a Mesh
Id | u | T | q
5 | {0.02, 0.01} | 130 | 27
1
2
3
4
5
6
7
State Vars.
Node Attribute
7
Column Metadata
Id: q
Type: Node attr.
Unit: mW/m2
Data type: Scalar
Descript.: Heat flux
. . .
Id | Rho | K | cp
Shale (1) | 2700 | 3.95 | f(T)
Sand (2) | 2720 | 1.64 | f(T)
Properties
User Function
function f(T)
return .....
end
Node associated data
Cell associated properties

## Slide 20: Data associated to a Mesh
Id | P.I. | Phi
6 | 2 | 0.27
6 | 3 | 0.29
Gauss Point Attribute
1
2
4
5
6
3
3 * 6
Id | Ro
5 | 0.15
Cell Attribute
1
2
4
5
6
3
6
1
2
3
4
5
6
7
State var. “T” with a 4 level History
t=3s
t=2s
t=1s
t=0s
T3
83
T2
95
T1
112
Id | u | T0 | q
5 | {0.02, 0.01} | 130 | 27
Cell associated attributes
Gauss point associated attributes
History associated with mesh nodes

## Slide 21: Main classes: Meshes and associated entities
Mesh
Cell
Element
Cell Geometry
Shape
Cell Boundary
Integration Rule
Property Set
Element Mesh
Topo Cell Mesh
Border Integration Rule
n
n
n
Topo Element Mesh
n
1
1
n
Cell Mesh
n

## Slide 22: Accessing mesh associated data
Access to data in a simple and unique way
Abstract user functions
Storage independent
Version independent (history)
Single access way for scalar, vector or matrix data
Automatic unit conversion
ValueAccessor
  value()
  setValue()

## Slide 23: Main classes: Data access
Mesh
1
Cell Mesh
MValue Set
Value Info
Cell Accessor
Gauss Accessor
n
n
n
n
n
1
1
1
Element Mesh
Accesses
Creates
User Function
1
n
Value Data Storage
User Function Evaluator
1
Value Accessor
Creates
Value Set
Property Set

## Slide 24: State Variables
Physical values calculated by the simulation
Degrees of freedom
Defined in the spatial domain
One state variable can be associated to multiple meshes
Model Data
User Functions
Boundary Conditions
Property Sets
State Variable
Meshes
Initial Conditions

## Slide 25: Property Sets
Tables with properties
Each mesh cell is linked to a line in each table
Similar to the attribute concept
  Implementation difference
Id | Rho | K | cp
Shale (1) | 2700 | 3.95 | f(T)
Sand (2) | 2720 | 1.64 | f(T)
Properties
Model Data
User Functions
Boundary Conditions
Property Sets
State Variable
Meshes
Initial Conditions

## Slide 26: Initial Conditions
State variable values at the beginning of a simulation
Can be defined directly in the model description or through an initialization process during the orchestration
Model Data
User Functions
Boundary Conditions
Property Sets
State Variable
Meshes
Initial Conditions

## Slide 27: Boundary Conditions
Additional information added to the model to guarantee that its equations have an unique solution
Can be applied over
  Nodes
  Cells
  Borders (edges in 2D, faces in 3D)
General syntax, semantics interpreted by physics
Model Data
User Functions
Boundary Conditions
Property Sets
State Variable
Meshes
Initial Conditions

## Slide 28: User Functions
Can be associated with mesh attributes, properties or boundary conditions
Implemented in Lua or in C++
Access to mesh associated data
  Interpolations and unit conversions are done automatically
Id | Rho | K | cp
Shale (1) | 2700 | 3.95 | f(T)
Sand (2) | 2720 | 1.64 | f(T)
Properties
User Function
function f(T)
return .....
end
Model Data
User Functions
Boundary Conditions
Property Sets
State Variable
Meshes
Initial Conditions

## Slide 29: Example
Felippa, section 21.6
bridge.lua
1 – Simulation description
2 Simulation {
3 name = ’Bridge’,
4 description = ’Bridge model based on Felippa, example found ’..
5 ’in section 21.6, figures 21.13 through 21.16’
6 }
7
8 dofile(’$SIMULATIONDIR/$SIMULATIONNAME_model.lua’)
9 dofile(’$SIMULATIONDIR/$SIMULATIONNAME_solution.lua’)

## Slide 30: Example – bridge_model.lua (1/5)
1 -- State variables
2 StateVar {id = ’ux’, description = ’Displacement in the X direction’, format = ’8.4f’}
3 StateVar {id = ’uy’, description = ’Displacement in the Y direction’, format = ’8.4f’}
4
5 -- Sets of properties associated to model elements
6 PropertySet {
7 id = ’MatProp’,
8 typeName = ’GemaStdPropertySet’,
9 description = ’Material parameters’,
10
11 properties = {
12 {id = ’E’, description = ’Elasticity modulus’},
13 {id = ’A’, description = ’Cross section area’},
14 },
14 values = {
16 {id = ’Bottom’, E = 1000, A = 2.0},
17 {id = ’Top’, E = 1000, A = 10.0},
18 {id = ’Batten’, E = 1000, A = 3.0},
19 {id = ’Diagonal’, E = 1000, A = 1.0},
20 }
21 }
Standard description for a data set:
id
description
dim
unit
functions
sparse
defVal
history
ruleSet
format

## Slide 31: Example – bridge_model.lua (2/5)
24 -- List of mesh node coordinates (X, Y)
25 local mesh_nodes = {
26 { 0.0, 0.0}, {10.0, 5.0}, {10.0, 0.0}, {20.0, 8.0},
27 {20.0, 0.0}, {30.0, 9.0}, {30.0, 0.0}, {40.0, 8.0},
28 {40.0, 0.0}, {50.0, 5.0}, {50.0, 0.0}, {60.0, 0.0},
29 }
30
31 -- List of nodes and properties per mesh element
32 local mesh_elements = {
33 { 1, 3, MatProp = ’Bottom’ },
34 { 3, 5, MatProp = ’Bottom’ },
35 { 5, 7, MatProp = ’Bottom’ },
36 { 7, 9, MatProp = ’Bottom’ },
37 { 9, 11, MatProp = ’Bottom’ },
38 {11, 12, MatProp = ’Bottom’ },
39 { 1, 2, MatProp = ’Top’ },
40 { 2, 4, MatProp = ’Top’ },
41 { 4, 6, MatProp = ’Top’ },
42 { 6, 8, MatProp = ’Top’ },
43 { 8, 10, MatProp = ’Top’ },
44 {10, 12, MatProp = ’Top’ },
45 { 2, 3, MatProp = ’Batten’ },
46 { 4, 5, MatProp = ’Batten’ },
47 { 6, 7, MatProp = ’Batten’ },
48 { 8, 9, MatProp = ’Batten’ },
49 {10, 11, MatProp = ’Batten’ },
50 { 2, 5, MatProp = ’Diagonal’},
51 { 4, 7, MatProp = ’Diagonal’},
52 { 7, 8, MatProp = ’Diagonal’},
53 { 9, 10, MatProp = ’Diagonal’},
54 }
Tables with mesh node and cell definitions can be dynamically constructed through functions

## Slide 32: Example – bridge_model.lua (3/5)
56 – Mesh definition
57 Mesh {
58 -- General plugin attributes
59 id = ’bridgeMesh’,
60 typeName = ’GemaStdMesh.elem’,
61 description = ’Bridge mesh discretization’,
62
63 -- Number of coordinate dimensions
64 coordinateDim = 2,
65
66 -- Lists with state vars. stored per node and
67 -- properties stored per mesh element
68 stateVars = {’ux’, ’uy’},
69 cellProperties = {’MatProp’},
70
71 -- Geometry
72 nodeData = mesh_nodes,
73 cellData = {{cellType = ’bar2’, cellList = mesh_elements}},
74 }
Standard fields, common to all plugin types
Fields interpreted by the GemaStdMesh plugin

## Slide 33: Example – bridge_model.lua (4/5)
76 -- Boundary conditions
77 BoundaryCondition {
78 id = ’bc1’,
79 description = ’External forces applied to model nodes’,
80 type = ’node forces’,
81 mesh = ’bridgeMesh’,
82
83 properties = {
84 {id = ’f’, description = ’External force applied on the node’, dim = 2},
85 },
86
87 nodeValues = {
88 -- node, fx, fy
89 { 3, {0.0, -10.0}},
90 { 5, {0.0, -10.0}},
91 { 7, {0.0, -16.0}},
92 { 9, {0.0, -10.0}},
93 {11, {0.0, -10.0}},
94 }
95 }

## Slide 34: Example – bridge_model.lua (5/5)
97 -- Boundary conditions (continued)
98 BoundaryCondition {
99 id = ’bc2’,
100 description = ’Prescribed node displacements’,
101 type = ’node displacements’,
102 mesh = ’bridgeMesh’,
103
104 properties = {
105 {id = ’ux’, description = ’Fixed node displacement in the X direction’, defVal = -9999},
106 {id = ’uy’, description = ’Fixed node displacement in the Y direction’, defVal = -9999},
107 },
108
109 nodeValues = {
110 -- node, ux, uy
111 { 1, 0.0, 0.0}, -- Node fixed in both directions
112 {12, nil, 0.0}, -- Node fixed in y but free to move in x
113 }
114 }

## Slide 35: Simulation Components
Model Data
Solution Method
Results Monitor
Simulation
Notes: Dados do Modelo = O que?
Método de Solução = Como?

## Slide 36: Solution method – How it will be simulated ?
Solution Method
Numeric Solvers
Physics
Processes
function script()
end
Orchestration Script

## Slide 37: Orchestration Script
Defines the sequence of executed processes
Main simulation loop
Using Lua allows:
  The use of complex operations as needed
  Configurable by users with limited programming experience
Solution Method
Numeric Solvers
Physics
Processes
function script()
end
Orchestration Script

## Slide 38: Processes
Solution Method
Numeric Solvers
Physics
Processes
function script()
end
Orchestration Script
High level action executed by the orchestration script
Implemented in C++ or in Lua
Data transfer between meshes
Processes
Mesh refinement/ reorganization
Finite Element Analysis
Analysis by other methods
Connection with external simulators
Data Input and Output
. . .

## Slide 39: Orchestration Examples
Temperature Calculation
Save results
Init. transient analysis
t = 0s
Save results in t
Temperature calculation at time t
t = t + Δt
Initial Temperature Calculation
Deposition and decompaction calculation
Porosity calculation
Init. transient analysis
t = 0s
Temperature calculation at time t
Ro Calculation
HC conversion rate calculation
Residue Calculation
t = t + Δt
Save results in t
Update mesh if a new layer was deposited
Error > tolerance
Non-linear loop
Thermal cond. = k(φ, T, Sw)

## Slide 40: FEM Process
Finite Element Analysis
Numeric Solver
Physics
Mesh
State Variables (DOF)
Boundary Conditions
Initial Conditions

## Slide 41: Physics
Specialize analysis processes for a set of discrete equations
Each analysis process type has specific interfaces
FEM Physics
  Define, for each element, local matrices that will be combined in the global stiffness matrix
  Multiple physics can cooperate in the solution of a tightly coupled problem
Solution Method
Numeric Solvers
Physics
Processes
function script()
end
Orchestration Script

## Slide 42: Physics x Processes
Steps needed in a FEM analysis are basically the same, independently of the equations being solved.
  The distinction between a stress and a temperature analysis are basically the equations that are solved to calculate local element matrices.
In GeMA:
  The global steps of a FEM analysis are the process
  The routines used to calculate local element matrices are the physics
Solution Method
Numeric Solvers
Physics
Processes
function script()
end
Orchestration Script

## Slide 43: Breaking a coupled Physics
(u1, T1)
(u2, T2)
(u3, T3)
u
1 2 3
T
1 2 3
1
u 2
3
1
T 2
3
uij
Tij
uiTj
Tiuj
Coupled Physics
Physics:
Displacements
+
Temperature
+
Coupling
uij = u’ij + u”ij
Tij = T’ij + T”ij
with
u”ij
T”ij
uiTj
Tiuj
u'ij
T'ij
+
+

## Slide 44: FEM Process steps
1) Initialize Assembler
2) Create global matrices and vectors
3) Fill matrices and vectors
4) Solve the linear system K . x = f
5) Save results
6) Derived results calculation
3.2) Get boundary condition contributions, by element and by physics.
Ke
fe
K
f
3.1) Get element contributions, by physics.
3.3) Remove degrees of freedom due to “Dirichlet” conditions
Assembler
Ke
fe
Assembler
Physics
Physics

## Slide 45: Physics for temperature calculation in C++
1 bool HeatPhysics::fillElementData(const Element* e,
2 FemMatrixSet& elemMatrices,
3 FemVectorSet& elemVectors)
4 {
5 const Shape* shape = e->shape();
6 int n = e->numNodes(); // Number of elem nodes
7 int ndim = _nodeAccessor->valueSize(); // Node coord dimension
8
9 // Get a reference for element K and f, filling them with zeros
10 Matrix& elemK = elemMatrices.useMatrix(FemMatrix_K);
11 Vector& elemF = elemVectors.useVector(FemVector_Fe);
12 elemK.zeros(); // Size = (n x n)
13 elemF.zeros(); // Size = (n)
14
15 // Fills the matrix X with node coordinates (size = n x ndim)
16 Matrix X;
17 e->fillNodeMatrix(_nodeAccessor, X);
18
19 // Aux values needed in the calculation:
20 Matrix B; // The shape function cartesian partials matrix
21 // (size = ndim x n)
22 Vector N; // The shape functions vector (size = n)
23 CRMatrix cond; // The conductivity matrix (size = ndim x ndim)
24 double t = 1.0; // Element thickness for 2D elements
25 double G; // Internal element heat generation rate
26 Vector ip; // Integration point natural coordinates
27 double w; // The Gauss point weight
28 double detJ; // The determinant of the Jacobian matrix
29
30 // Gets the element Gauss rule and loops over integration points
31 const IntegrationRule* ir = elementIntegrationRule(e->type());
32 for(int i = 0, nip = ir->numPoints(); i<nip; i++)
33 {
34 // Get the integration point & weight
35 ir->integrationPoint(i, ip, &w);
36
37 // Get needed element properties
38 _kAccessor->matrixValueAt(e, &ip, cond, i);
39 G = _generationRateAccessor->scalarValueAt(e, &ip, i);
40 if(ndim == 2)
41 t = _planeWidthAccessor->scalarValueAt(e, &ip, i);
42
43 // Fill the N (column) vector and Calc B matrix and detJ.
44 shape->shapeCartesianPartials(ip, X, B, &detJ, true);
45 shape->shapeValues(ip, N);
46
47 // Calculate values
48 double c = w * t * detJ;
49 elemK += B.t() * cond * B * c;
50 elemF += N * (c * G);
51 }
52 return true;
53 }

## Slide 46: Physics for temperature calculation in Lua
24 -- Get the Gauss point contribution for the stiffness matrix
25 local function fillElemData()
26 -- Get the conductivity matrix from the k value (isotropic
27 -- case) or from k(1) and k(2) (anisotropic case)
28 local kx = (type(k) == ’number’ and k) or k(1)
29 local ky = (type(k) == ’number’ and k) or k(2)
30 local Cond = Matrix{{kx, 0}, {0, ky}}
31
32 -- Calculates the returned matrix (true means that it is symmetric)
33 return B:t() * Cond * B * t, true
34 end
35
36 -- Function for filling an elements local matrix based on the fillElemData()
37 -- auxiliary function. The first parameter defines the data that will be
38 – automatically available to the function.
39 TPhysics.fillElementData = CreateFillElementDataFunction({’k’, ’t’, B = true}, fillElemData)

## Slide 47: Numeric Solvers
Solves (linear) equation systems
Responsible for providing the matrix used to store the global equation system
Armadillo
  Complete matrices: Lapack
  Sparse matrices: SuperLU
Solution Method
Numeric Solvers
Physics
Processes
function script()
end
Orchestration Script

## Slide 48: Process to transfer data between meshes
1
2
3
Source Mesh
Destination Mesh
1
2
3
Search the source mesh element containing the destination mesh node.
Field interpolation at the node position
Transfer of the interpolated value to the destination mesh

## Slide 49: Example – bridge_solution.lua
1 -- Used physics
2 PhysicalMethod {
3 id = ’stressPhysics’,
4 typeName = ’ GemaStdMechanics.bar’,
5 type = ’fem’,
6
7 mesh = ’bridgeMesh’,
8 boundaryConditions = {’bc1’, ’bc2’},
9 }
10
11 -- Used numerical solver
12 NumericalSolver {
13 id = ’solver’,
14 typeName = ’GemaStdNumSolver’,
15 description = ’Standard matrix solver’,
16 }
17
18 -- Orchestration script
19 function ProcessScript()
20 fem.solve({’stressPhysics’}, ’solver’)
21
22 utils.print(’Calculated results:’)
23 utils.printMeshNodeData(’bridgeMesh’, {’ux’, ’uy’})
24 utils.print(’’)
25 utils.printMeshCellData(’bridgeMesh’, ’s’)
26 end

## Slide 50: Test 1: Temperature
Heat conduction in a plate
Analytical solution used to validate results:
T(x, y) = ?
1m
1m
100 oC
100 oC
100 oC
500 oC
k = 10 W/(m. oC)

## Slide 51: Test 1: Temperature
1 -- Auxiliary functions used to create node and triangle lists forming a
2 -- mesh with nx/ny nodes in each direction, spaced by dx/dy.
3 local function createNodeList(dx, nx, dy, ny)
4 local nodes = {} -- {x, y, Tana}
5 for y=0, ny-1 do
6 for x=0, nx-1 do
7 nodes[#nodes+1] = {x*dx, y*dy, T(x*dx, y*dy)}
8 end
9 end
10 return nodes
11 end
12
13 local function createElementList(dx, nx, dy, ny)
14 local N = function (r,c) return (r-1)*nx + c end
15 local cells = {}
16 for y=1, ny-1 do
17 for x=1, nx-1 do
18 cells[#cells+1] = {N(y, x), N(y, x+1), N(y+1, x)}
19 cells[#cells+1] = {N(y, x+1), N(y+1, x+1), N(y+1, x)}
20 end
21 end
22 return cells
23 end
24
25 -- User function to calculate error values
26 NodeFunction { id = ’errf’,
27 parameters = { {src = ’Tana’, unit = ’degC’},
28 {src = ’T’, unit = ’degC’},
29 },
30 method = function(Tana, T)
31 return math.abs(Tana - T)
32 end
33 }

## Slide 52: Test 1: Temperature
16 Mesh {
17 -- General attributes
18 id = ’plateMesh’,
19 typeName = ’GemaStdMesh.elem’,
20 description = ’Plate mesh discretization’,
21
22 -- Problem dimension and coordinate unit
23 coordinateDim = 2,
24 coordinateUnit = ’cm’,
25
26 -- Lists with state variables and attributes stored per mesh node and
27 -- properties stored per mesh element
28 stateVars = {’T’},
29 cellProperties = {’MatProp’},
30 nodeAttributes = {
31 {id = ’Tana’, description = ’Analytical value’, unit = ’degC’},
32 {id = ’Err’, description = ’Error’, unit = ’degC’,
33 functions = true, defVal = ’errf’, format = ’10.4’}
34 },
35
36 -- Geometry
37 nodeData = createNodeList(w/(nx-1), nx, h/(ny-1), ny),
38 cellData = {{cellType = ’tri3’, MatProp = 1,
39 cellList = createElementList(w/(nx-1),nx,h/(ny-1),ny)}},
40 boundaryEdgeData = {
41 {id = ’bottom and sides’, cellList = otherBorders(nx,ny)},
42 {id = ’top’, cellList = topBorder(nx,ny)},
43 }
44 }

## Slide 53: Test 1: Temperature
18 -- Orchestration script
19 function ProcessScript()
20 -- Executes a finite element analysis, receiving as
21 –- parameters a physics and a numeric solver
22 fem.solve({’HeatPhysics’}, ’solver’)
23
-- Saves the state variable ’T’ and attribute ’err’,
-- associated with nodes from mesh ’plateMesh’ in
-- the file results.nf
27 utils.saveMeshFile(’plateMesh’, ’./results.nf’,
28 ’nf’, {’T’, ’Err’})
29 end
1 -- Orchestration script
2 function ProcessScript()
3 -- Creates the file that will store saved results
4 local file = utils.prepareMeshFile(’plateMesh’,
5 ’./results.nf’, ’nf’, {’T’})
6
7 -- 1ms time step. Total simulation duration = 0.2s
8 local dt = 0.001
9 local endt = 0.2
10 local nsteps = endt / dt
11
12 -- Initializes transient analysis
13 local solver = fem.initTransientSolver({’HeatPhysics’}, ’solver’)
14
15 -- Temporal loop
16 for i=1, nsteps do
17 -- Calculates temperature after a time step = dt
18 fem.transientStep(solver, dt)
19
20 -- Updates the current simulation time
21 setCurrentTime(i*dt)
22
23 -- Adds results to the file
24 utils.addResultToMeshFile(file, i*dt)
25 end
26 utils.closeMeshFile(file)
27 end
Steady state analysis
Transient analysis

## Slide 54: Test 1: Temperature
T(oC)
Error(oC)
T(oC)
t = 0.01s
t = 0.20s
t = 0.10s

## Slide 55: Test 2: Solidification
Chart: Temperature profile in x = 1
t = 2 s
t = 4 s
Mushy
Solid
Mushy
Solid
0
-5
-10
-15
-20
-25
-30
-35
-40
-45
T(oC)
-45.0 oC
-0.15 oC
4
0.5
Full
Without non-linear step
Without phase change

## Slide 56: Test 2: Solidification
1 -- User function to calculate the effective specific heat capacity
2 CellFunction { id = ’ceff’,
3 parameters = { {src = ’T’, unit = ’degC’},
4 {src = ’Ts’, unit = ’degC’},
5 {src = ’Tl’, unit = ’degC’},
6 {src = ’cs’, unit = ’J/(kg.degC)’},
7 {src = ’cl’, unit = ’J/(kg.degC)’},
8 {src = ’cf’, unit = ’J/(kg.degC)’},
9 {src = ’L’, unit = ’J/kg’},
10 },
11 method = function(T, Ts, Tl, cs, cl, cf, L)
12 if T < Ts then
13 return cs
14 elseif T >= Tl then
15 return cl
16 else
17 return cf + L / (Tl - Ts)
18 end
19 end
20 }

## Slide 57: Test 2: Solidification
1 function ProcessScript()
2 -- Creates the file that will receive the saved results
3 local file = utils.prepareMeshFile(’mesh’, ’./results.nf’, ’nf’, {’T’})
4
5 -- 50ms time step. Total simulation duration = 5s
6 local dt = 0.05
7 local endt = 5
8 local nsteps = endt / dt
9
10 -- Initializes a non-linear transient analysis
13 local solver = fem.initTransientSolver({’HeatPhysics’}, ’solver’, {}, true)
15
16 -- Temporal loop
17 for i=1, nsteps do
18 -- Non-linear loop
19 local j = 1
20 while j <= 10 do
21 -- Executes a step
22 fem.transientLinearStep(solver, dt, j)
23
24 -- Calculates residue
25 r = fem.transientLinearResidual(solver, dt)
26
27 -- Converged?
28 if r <= 1e-3 then
29 break
30 end
31 j = j + 1
32 end
33 assert(j <= 10, ’Failed to achieve convergence’)
34
35 -- Adds results to the file
36 utils.addResultToMeshFile(file, i*dt)
37 end
38 utils.closeMeshFile(file)
39 end

## Slide 58: Coupled test: Stress - Temperature
T(oC)
Temperature and Deformation (exaggeration = 10x)
T = 100.0 oC
1 m
5 m
q = 100 W/m2
q=0
q=0
q=0
q=0
α = 2e-5 / oC
α = 10e-5 / oC
0.5 m
1 m

## Slide 59: Coupled test: Stress - Temperature
31 – Boundary conditions for stress and temperature
32 BoundaryCondition {
33 id = ’Tbc1’,
34 type = ’fixed temperature’,
35 mesh = ’mesh’,
36 properties = { {id = ’T’, unit = ’K’} },
37 nodeValues = { {’topBorder’, 100} },
38 }
39 BoundaryCondition {
40 id = ’Tbc2’,
41 type = ’fixed heat flux’,
42 mesh = ’mesh’,
43 properties = { {id = ’q’, unit = ’W/m2’} },
44 edgeValues = { {’bottomHeatedBorder’, -100} },
45 }
46 BoundaryCondition {
47 id = ’ubc’,
48 type = ’node displacements’,
49 mesh = ’mesh’,
50 properties = { {id = ’ux’, defVal = -9999},
51 {id = ’uy’, defVal = -9999} },
52 nodeValues = { {’rightBorder’, 0.0, 0.0} },
53 }

## Slide 60: Coupled test: Stress - Temperature
1 -- Numerical solver used
2 NumericalSolver {
3 id = ’solver’,
4 typeName = ’GemaStdNumSolver’,
5 description = ’Simple matrix solver’,
6 }
7
8 -- Physics for temperature calculation
9 PhysicalMethod {
10 id = ’HeatPhysics’,
11 typeName = ’GemaStdHeatPhysics’,
12 type = ’fem’,
13
14 mesh = ’mesh’,
15 boundaryConditions = {’Tbc1’, ’Tbc2’},
16 }
17
18 -- Physics for stress and displacement calculation
19 PhysicalMethod {
20 id = ’StressPhysics’,
21 typeName = ’GemaStdStressPhysics.plate’,
22 type = ’fem’,
23
24 mesh = ’mesh’,
25 boundaryConditions = {’ubc’},
26 skipStress = true, -- Stresses are calc. by the coupling physics
27 properties = {h=’t’}, -- Property name translation. Physics expects
28 -- that the width is named ’h’
29 }
30
31 -- Physics for stress – temperature coupling
32 PhysicalMethod {
33 id = ’TempStressPhysics’,
34 typeName = ’GemaStdStressPhysics.plateTemperature’,
35 type = ’fem’,
36
37 mesh = ’mesh’,
38 properties = {h = ’t’},
39 referenceT = 100, -- Reference temperature for the material
40 }
41
42 -- Orchestration script
43 function ProcessScript()
44 -- Executes a FEM coupled analysis. The 3 physics given as
45 -- parameters cooperate in the building of the global matrix
46 fem.solve({’HeatPhysics’, ’StressPhysics’, ’TempStressPhysics’},
47 ’solver’)
48
49 -- Save state variables and stress values calculated at Gauss
50 -- points in the results.nf file
51 utils.saveMeshFile(’mesh’, ’./results.nf’, ’nf’, {’ux’,’uy’,’T’},
52 {’sxx’, ’syy’, ’sxy’, ’s1’, ’s2’},
53 {saveDisplacements=true})
54 end

## Slide 61: End...
Questions?
cmendes@tecgraf.puc-rio.br